## Slide 1: Overview of Wastewater Treatment Processes
SUSANTI RINA N,ST,M.Eng

## Slide 2: PENGOLAHAN AIR LIMBAH
AIR LIMBAH :
Kontaminan Fisis :
Large solid objects
Suspended solids
Kontaminan Kimiawi:
  Biodegradable organics
  Nutrients
  Refractory chemicals
  Heavy metals
  Dissolved inorganic solids
Kontaminan Biologis:
  Pathogens
Waste Water Treatment
(WWT)
Air yang diolah:
Disposed of in environment
Reuse/recycle

## Slide 3: The objective of WWT
Tujuan utama pengolahan air limbah pada umumnya memungkinkan limbah manusia dan industri dibuang tanpa membahayakan kesehatan manusia atau merusak lingkungan dan alam.

## Slide 4: WWT methods
Conventional WWT
  Preliminary treatment
  Primary treatment
  Secondary treatment
  Tertiary/advanced treatment
  Disinfection
Natural biological treatment systems
  Wastewater stabilization ponds
  Overland treatment of Wastewater
  Macrophyte treatment
  Nutrient film technique

## Slide 5: Conventional WWT
Pengolahan air limbah konvensional terdiri dari kombinasi proses fisik dan kimiawi dan proses biologis serta operasi untuk menghilangkan zat padat, bahan organik dan kadang-kadang nutrien pada air limbah.

## Slide 7: Preliminary treatment
Tujuan pengolahan pendahuluan adalah pemindahan padatan kasar dan bahan besar lainnya yang sering ditemukan di air limbah.
Preliminary treatment operations typically include:
  coarse screening,
  grit removal,
  comminution of large objects (only in some cases).

## Slide 8
Bar screen digunakan pada tahap paling awal dari pengolahan air limbah.

## Slide 9
Bar screen
Grit Chamber
IPAL Sewon, Bantul

## Slide 10
Sucking hose to remove grit & sand
IPAL Sewon, Bantul

## Slide 11
Sand & grit removed
IPAL Sewon, Bantul

## Slide 12
A comminutor used to grind up large solids.

## Slide 13: Primary treatment
Tujuan primary treatment adalah menghilangkan padatan organik dan anorganik yang dapat mengendap dengan sedimentasi, dan pengangkatan bahan yang mengapung (sampah).
Sekitar 25 sampai 50% kebutuhan Biological Oxygen Demand yang masuk (BOD5), 50 sampai 70% total padatan tersuspensi (SS), dan 65% minyak dan lemak dikeluarkan selama primary treatment.
Beberapa organic nitrogen, organic phosphorus, and heavy metals yang terkait dengan padatan juga dilepaskan selama sedimentasi primer namun konstituen koloid dan terlarut tidak terpengaruh..

## Slide 14
Rectangular settling tank.

## Slide 15
Circular settling tank.

## Slide 16: Secondary treatment
Tujuan secondary treatment adalah perlakuan lebih lanjut dari efluen dari primary treatment untuk menghilangkan sisa organik dan padatan tersuspensi.
Dua kategori dari Secondary Treatment :
  Low rate processes: bak aerasi, kolam stabilisasi
  High rate processes: lumpur aktif, trickling filters, rotating biological contactors.
High-rate biological processes dicirikan oleh volume reaktor yang relatif kecil dan konsentrasi mikroorganisme yang tinggi dibandingkan dengan low rate processes.

## Slide 17: Secondary treatment
High-rate biological treatment processes, dikombinasikan dengan sedimentasi primer, biasanya menghilangkan 85% BOD5 dan TSS yang semula ada di air limbah dan beberapa logam berat.
Akan tetapi, hanya sedikit phosphorus, nitrogen, non-biodegradable organics, or dissolved minerals yang ikut terbuang.

## Slide 18: Secondary treatment
Aerobic process
  Suspended growth : activated sludge
  Attached growth : RBC, Trickling filter
  Hybrid (combination)
Anaerobic process
  Suspended growth : anaerobic digester
  Attached growth : packed bed & fluidized bed
  Sludge blanket : UASB
  Hybrid (combination of suspended & attached)

## Slide 19
Activated sludge

## Slide 20: Activated sludge with Sequencing Batch Reactor (SBR)
SBR in IPAL RSUD Wates

## Slide 21
Trickling filters
Wastewater
Treated water
Circulating wastewater sprayer

## Slide 22
Rotating biological
contactors

## Slide 23: Anaerobic digestion

## Slide 24: Anaerobic packed bed
Wastewater
Biogas
Treated water

## Slide 25: Anaerobic fluidized bed

## Slide 26: Upflow anaerobic sludge blanket